## Slide 1: Emf and internal resistance
(m) define e.m.f. in terms of the energy transferred by a source in driving unit charge round a complete circuit
(n) distinguish between e.m.f. and p.d. in terms of energy considerations
(o) show an understanding of the effects of the internal resistance of a source of e.m.f. on the terminal potential difference and output power.

## Slide 2: Need to know
Questions may be on combinations of resistors and also complete circuits involving internal resistance.
be able to recognize and use the accepted circuit symbols.

## Slide 3: Recall - Energy and work in an electric circuit
Look at a cell connected to a lamp.
The charge carriers are pushed around a circuit by the emf of the cell.
The charge carriers are like water in a hydroelectric power station - they do work (e.g. in the lamp) just as the flowing water does work in the turbo-generators.
Neither the charge nor the water is ‘used up’ but it does lose potential energy.
In the power station, water loses gravitational potential energy by moving from higher GPE to lower GPE.
In an electric circuit the charge ‘falls’ from high electrical potential energy to lower electrical potential energy.
a cell provides a potential difference and that charges move around the circuit from higher to lower potential (negative charges ‘fall’ from - to + whilst positive charges would ‘fall’ the other way!).
The greater the vertical drop in the hydroelectric station the greater the change in potential energy per kilogram of water.
The higher the emf across a source of electrical energy the greater the change in potential energy per coulomb of charge moving between its terminals.

## Slide 4: Internal resistance
There are three ways to arrive at the equation relating emf, terminal pd, current and internal resistance. It is worth discussing all three, to show their equivalence
CELL
Terminal Voltage
e.m.f
‘lost volts’
R
r
E
I

## Slide 5: To do
Carry out experiment(s) to find the internal resistance of a power source.
Complete the worksheet

## Slide 6: Solutions
1. The two 1.5 V cells provide an emf of 3 V in series. If the current flowing is 0.5 A as stated, then for the potential difference across the internal resistance to be 0.5 V (that is, 3 V–2.5 V) the internal resistance of the cells combined would need to be 1Ω. The cells are in series so the resistance of each is 0.5 Ω.
2. The battery must have a low internal resistance so as to be able to deliver a current of 80 A from an emf of only 12 V. If the internal resistance is 0.05 Ω then the potential difference across this with a current of 80 A flowing is 4 V. Thus the potential difference across the 12 V battery drops to 8 V. This is a big enough change to dim headlights rated at 12 V.
3. The maximum current is 60 mA. A torch bulb has a resistance of only a few ohms, so connected across such a supply the potential difference across it would be very near to zero, with a current of only 60 mA through it.
4. The 1000 Ω voltmeter draws a current from the cell, of 1 mA when it reads 1.0 V. If the cell has internal resistance some of its emf will be used in driving the current through the cell. A voltmeter with very high resistance draws very little current, and reads nearer to the emf of the cell. If the emf is 1.2 V then 0.2 V is used in driving the current of
1 mA through the internal resistance, which is therefore 200 Ω.

## Slide 7: Voltage around a circuit
r
IR
E
r
E
(resourcefulphysics.org)

## Slide 8: More about the practical importance of internal resistance
What happens if a 1.5 V cell is shorted - i.e. its terminals are connected together by a wire of zero resistance?
You might think I = V / R with R = 0 should mean that an infinite current would flow (limited by other physical factors!)
But remember the internal resistance r. This limits the cell to a maximum (short-circuit) current of: I = E / r
We can use this to prevent EHT supplies giving the user an unpleasant shock. The series ‘internal’ resistance. Of an EHT supply is usually 5 MΩ.
These supplies are designed to provide a high voltage to a high resistance load (e.g. cathode ray tube) but if the terminals or wires connected to them were accidentally touched this could provide a nasty shock (lower resistance in the load and higher current). One way to deal with this is to connect a large resistance in series with the output (positive) terminal. If the terminals are shorted (e.g. by contact through a person) the current drawn is limited to I = E / r. A typical EHT supply (up to 5000 V) is protected by a 5 MΩ resistor so the maximum current if shorted is just 1 mA. That shouldn’t kill you! Be aware however that HT supplies (0-300 V) have a much lower internal resistance, and could kill you, so special shrouded leads should be used.
EHT supplies often have a further ‘safety resistor’ (e.g. 10 MΩ) to reduce the maximum current still further. This resistor can be by-passed when necessary. No school EHT supply is allowed to provide more than 5 mA.

## Slide 9: Power
ΔW = V ΔQ
and ΔQ = I Δt
ΔW = I VΔt
The rate of doing work is the power:
P = ΔW / Δt = I V
What is the power of:
A lamp connected to 230 V (ac) supply
100W
an electric kettle
about 2.0 kW
power station
~1.0 GW along transmission lines so need to transmit at high voltage in order to reduce losses due to heating.

## Slide 10: Ideal ammeters
In order to measure the current, an ammeter is placed in series, in the circuit.
What effect might this have on the size of the current?
The ideal ammeter has zero resistance, so that placing it in the circuit does not make the current smaller.
Real ammeters do have very small resistances ‑ around 0.01 Ω.

## Slide 11: Ideal voltmeters
A voltmeter is connected in parallel with a component, in order to measure the p.d. across it.
lWhy can this increase the current in the circuit?
lSince the voltmeter is in parallel with the component, their combined resistance is less than the component's resistance.
lThe ideal voltmeter has infinite resistance and takes no current.
lDigital voltmeters have very high resistances, around 10 MΩ, and so they have little effect on the circuit they are placed in.