Deflecting electron beams in a magnetic field

Circular control

Magnetic fields are often used to steer beams of charged particles, in situations from a television tube to a large-scale particle accelerator.

The paths are always helices, circles or spirals, as the force acting on the charged particles within the beam is always at right angles to their velocity

Here you look at circular paths, keeping it simple.

You will need:

- electron deflection tube

- stand for tube

- EHT power supply, 0–5 kV

- power supply, 5 V dc

- rheostat

- Helmholtz pair of coils

- 4 mm leads

|  | Safety Wire carefully, no bare conductor above 40 V Although the output form the EHT power supply will not give a fatal shock, it can still make the user jump and is quite unpleasant. Teltron tubes often use male 4mm connectors so the leads must terminate in female (socket) connectors if bare conductors are to be avoided. The protective resistor in the EHT can not be used here. |
| --- | --- |

Deflecting each electron

The deflection tube uses an electron gun to inject electrons into a region of nearly uniform magnetic field perpendicular to the beam. In this region a magnetic field acts on the charge, producing a uniform acceleration in the direction perpendicular to the magnetic field and to the velocity of the electrons. Each electron experiences an acceleration that is always at right angles to its velocity. You should recognise this as a recipe for circular motion by now.

Think carefully about the effect on the circle of the following changes:

	increasing the accelerating pd in the electron gun.

	increasing the current in the coils producing the magnetic field.

You might like to go further and predict how the curve will change when you double one quantity, then the other, perhaps building a computer model to check your predictions, if that helps.

Below is an image as a reminder of what you have seen. As further reinforcement of the analysis suggested you might like to:

	extract enough data to show that the path followed is a circle.

You have

1.	Seen electrons in circular motion.

2.	Thought about the principles behind this motion.

3.	Seen how an accelerating pd can be used to make an electron gun

Practical advice

You will need to set this demonstration up in a well darkened room for maximum effect. You will also want to think carefully about how to display both the tube, in order to explain this action, and the resulting circle, to the size of group that you will be showing it to. It is often a good idea to cover the back of the tube with a black cloth

If new to wiring up electron deflection tubes you may well also wish to practice beforehand, and have a small bench top lamp to hand, well shaded so as not to destroy the dark adaptation of the group’s eyes. You will need to explain and show the actions of the electron gun and the coils, probably using a gimballed bar magnet to show the direction of the field.

You will probably get a spread of circles, perhaps due to the field being non-uniform (a Helmholtz pair only produce an approximately uniform field in the central third of the volume they enclose), due to the electrons provided by the electron gun having a range of velocities, and due to random thermal motion superimposed on the velocity acquired from the action of the accelerating pd.

It may also help to connect both electric deflection plates to the anode in the electron gun and to earth, forcing the filament (cathode) to a large negative voltage.

NB: many low voltage power supplies must not have the output voltage adjusted while delivering high currents.

|  | Safety Wire carefully, no bare conductor above 40 V Although the output form the EHT power supply will not give a fatal shock, it can still make the user jump and is quite unpleasant. Teltron tubes often use male 4mm connectors so the leads must terminate in female (socket) connectors if bare conductors are to be avoided. The protective resistor in the EHT can not be used here. |
| --- | --- |

External references

This activity is taken from Advancing Physics chapter 16, 120D

Measuring the charge to mass ratio for an electron

Using circular motion

Using a magnetic field to drive an electron round in a circle can give information about the acceleration.

The magnetic force acting is

and the force required to drive it round in a circle is given by

You can put these two equal to get

So three measurements can give the charge / mass ratio of the electron. Both the radius of the circular motion and the magnetic field strength can be measured in a fairly straightforward way. The measurement of the velocity, however, is harder.

Electrons are accelerated by an electron gun. So

so at first sight it looks as if you need q and m to get started. However, maths comes to our aid, allowing you to combine the two sets of relationships to get

(arrange both relationships to give v2 then put them equal).

Now we can measure three things in the laboratory in order to find the charge to mass ratio for the electron.

By extension you measure the charge / mass ratio for any charged particle, allowing you to characterise many particles.

Deflection with electric and magnetic fields

Instructions and information

Write your answers in the spaces provided. Use these data:

- magnitude of the electronic charge = 1.6  10–19 C

- mass of electron = 9.1  10–31 kg

The force on an electric current in a magnetic field is perpendicular to both the current and the field. This diagram may help you.

Questions

A beam of particles passes in a straight line from a source X, to a spot, E, on a fluorescent screen. When the electromagnet shown is switched on, the beam hits the screen at one of the spots A, B, C, D or E.

1.	In which direction does the beam bend if the particles are positively charged?

2.	Where does it go if the particles are neutral?

3.	What happens to the positively charged particles if the magnetic field is reversed?

In one form of mass spectrometer, charged ions in the beam fan out, moving in the paths shown in the diagram. Parts of the paths include a magnetic field whose direction is perpendicular to the plane of the paper.

4.	Indicate places where there must be no magnetic field in the direction suggested. Do not 	use shading.

5.	Shade the area where there must be a magnetic field.

6.	What is the shape of the path followed by a proton that is projected into a uniform 	magnetic field at right angles to its velocity? Justify your answer.

The diagram shows the initial path of an electron fired into a uniform magnetic field. The magnetic field is at right angles to the direction of the electron and is directed away from the reader.

7.	Add a labelled arrow to the show the direction of the force on the electron.

8.	Draw the subsequent path of the electron.

A uniform electric field is produced by maintaining a potential difference of 1000 V across a pair of parallel plates 5 cm apart. An electron enters the field at right angles as shown with a velocity of 4.0  107 m s–1 and emerges from the plates without hitting them.

9.	Draw in the path of the electron on the diagram.

10.	What name is given to this type of path?

Hints

1.	Remember that the left-hand motor rule works for conventional current.

2.	Remember that the left-hand motor rule works for conventional current.

Practical Advice

These questions are intended to be straightforward, to reinforce understanding and to build confidence. Students will be required to understand the independence of vertical and horizontal motions, and also motion where the acceleration is constant.

External reference

This activity is taken from Advancing Physics chapter 16, 90S

The cyclotron

Background

In a cyclotron, protons are kept moving in a circular path by a uniform magnetic field at right angles to the plane of the path.

The American physicist E O Lawrence designed and built the first cyclotron in 1930. For this achievement, he was awarded the Nobel Prize for physics in 1939. Only a few centimetres in diameter, the Lawrence cyclotron accelerated protons to energies of 80 keV.

Questions

You will need the following data:

mass of proton = 1.7 x 10–27 kg

charge on proton = 1.6 x 10–19 C

1.	What is the velocity of a proton with an energy of 80 keV?

2.	The largest possible path had a radius of about 50 mm. What strength of magnetic field 	must have been used?

3.	What would be the radius of the path followed by a proton with half this maximum energy 	in the same field?

4.	How long would it take 80 keV protons to travel once round their path? How long would it 	take for those with half this energy?

Constructed of two D -shaped chambers (later called ‘dees’ because of their shape), the cyclotron worked by giving particles of any energy, on their respective paths, a push every time they had completed half an orbit.

5.	How was it possible for particles of differing energy all to be accelerated together?

Practical advice

This is something  more able students may enjoy thinking about.

It is instructive for students to realise that even such a crude and simple device represented a major advance in particle physics, providing a source of high-energy particles that could be fired at atomic nuclei, to probe their structure. Lawrence had done a calculation of the necessary length for a linear accelerator to produce protons with energies of a million eV. He realised his laboratory was too small, and that set him thinking about bending the accelerator so that protons would travel in a spiral. Each time the protons crossed the gap between ‘dees’, they would be accelerated. To make his cyclotron work, he needed a good vacuum in the chambers and very high-frequency electrical oscillator to alternate the polarity of the ‘dee’ chambers.

A key idea, that radius is proportional to speed, is accessible to analysis.

Half a century later Edwin McMillan, another great American particle physicist, said of the cyclotron: ‘I consider this to be the single most important invention in the history of accelerators; it brought forth a basic idea of great power, and one capable of later elaborations and variations … All the big proton synchrotrons are really just an extension of the cyclotron principle.

External reference

This activity is taken from Advancing Physics chapter 16, 100S

Charged particles moving in a magnetic field

Instructions

This question set contains two groups of questions. Answer all the questions in the spaces provided.  The following data will be needed:

	magnitude of the electronic charge = 1.6  10–19 C

	mass of electron = 9.1  10–31 kg

Questions 1– 5 are about the motion of charged particles in a bubble chamber.

1.	An electron gun in a vacuum accelerates electrons up to a kinetic energy of 2.9  10–16 J. 	Show that the speed acquired by each electron is 2.5  107 m s–1.

The electron beam enters a region of uniform magnetic field of strength, B, perpendicular to the beam. The magnetic field causes the beam to follow a circular path as in the diagram below.

2.	Show that the force experienced by the electron is about 8.8  10–15N,

when B is 2.210–3 T.

3.	Use your answer to question 2 to find the radius of this circular path.

4.	Evidence for the motion of electrons in magnetic fields can be observed from the trail of 	bubbles they leave as they pass through liquid hydrogen. In these bubble-chamber 	experiments a single electron tends to produce a track which is a spiral rather than a 	circle. Explain why.

5.	On the diagram below draw the likely path of a proton travelling at the same speed in an 	identical field.

Questions 6–10 are about the motion of charged particles in magnetic fields and the cyclotron frequency.

6.	Explain why a charged particle, moving with a constant speed v perpendicular to a 	uniform magnetic field B, will follow a circular path.

7.	Show that for a particle of mass m and charge q the radius of the circular path is given by 	the expression r = mv/Bq.

8.	Using your answer to question 7, show that the frequency of this circular motion, known 	as the cyclotron frequency, is given by the expression f = qB/2m.

9.	Some astrophysicists believe that the radio signals of 109 Hz reaching us from Jupiter are 	emitted by electrons orbiting in Jupiter’s magnetic field. Assuming the frequency of the 	radio emission is identical to the cyclotron frequency; find the strength of the magnetic 	field around Jupiter.

10	The electrons lose energy as they emit radiation. What effect, if any, will this have on the 	frequency of the radio signals detected? Explain your answer.

Hints

5.	Think about the charge and mass of the proton.

10.	What happens to the speed of the proton as it loses energy?

Practical advice

Both sets of questions link with work in particle physics. The radio emissions from electrons orbiting in the magnetic field of Jupiter are explained using the idea of cyclotron frequency.

External reference

This activity is taken from Advancing Physics chapter 16, 150S