## Slide 1: CT scanning
(f) Candidates should be able to show an understanding of the principles of CT scanning.
(g) Candidates should be able to show an understanding of how the image of an 8-voxel cube can be developed using CT scanning.

## Slide 2: X-ray: The beginning
X-Rays discovered in 1895 by Wilhelm Conrad Roentgen

## Slide 3: CT: The beginning
CT founded in 1970 by Sir Godfrey Hounsfield
  Engineer with EMI, LTD.
  first applications were in neuroradiology

## Slide 4: X-rays vs CT
Both CT and conventional x-rays take pictures of internal body structures. I
n conventional x-rays, the structures overlap. For example, the ribs overlay the lung and heart. In an x-ray, structures of medical concern are often obscured by other organs or bones, making diagnosis difficult.

## Slide 5: CT Scanner
X-Ray modality used to the body in cross section
Used to determine
  extent of trauma
  location and type of tumors
  status of blood vessels
  pre surgical planning

## Slide 6: CT System

## Slide 7: Basic CT scanner components
Gantry
X-Ray Tube
Detector
Control Console

## Slide 8: Gantry
CT X-ray tube
High voltage generator
Detector array
Data acquistion system
Slip ring

## Slide 9: Detector Elements
Capture energy that has not been attenuated by the patient

## Slide 10: CT
CT - Computed Tomography
CAT Scan - Computerized Axial Tomography

## Slide 11: Scanning methods
Surview
  AP,Lat
  Surview, Scanogram , Topogram….
Conventional CT
  Axial
    Start/stop
Volumetric CT
  Helical or spiral CT
    Continuous acquisition

## Slide 12: Building up an image
The section (or slice) through the body is divided up into a series of small units called voxels.
The image of each voxel would have a particular intensity, known as a pixel.
The pixels are built up from measurements of X-ray intensity made along a series of different directions around the section of the body.

## Slide 13: A 4 voxel section
This section is made up of 4 voxels.
Each voxel in the section has a particular intensity (the lower the intensity the more X-rays are absorbed.
(We do not know this before the scan)

## Slide 14: Building up an image
X-rays are directed at the sample from one direction.
And the measurement of intensity taken

## Slide 15
Total intensity direction 1 recorded
It is not known how much each voxel contributes to the intensity.

## Slide 16: Repeat from 2nd direction

## Slide 17: And add to values

## Slide 18: Repeat

## Slide 19: And one more time

## Slide 20: Now to build up our voxels
Deduct the ‘background’ intensity. The sum of the intensities in each case (14 here)

## Slide 21
Divide by the number of extra views.
And there is your image
Now multiply by a few billion times to get a CT image!

## Slide 22: Advantages of CT scans
Better detail compared with ultrasonography.
Relatively quick compared with MRI scanning.
Most systems can be scanned, eg brain to leg.
painless non invasive procedure with good sensitivity to detect pathology of the head
superior to an MRI when evaluating skull fractures
Can provide detailed images of the brain nervous tissue
Much cheaper than an MRI an equally as fast
The motion artifacts are less of a problem with a CT scan compared to an MRI.
Can be performed in patients with implanted medical devices.